## Slide 1: Introduction of Ultra-wideband (UWB) Technology
Graham Zhu
Graham.zhu@nus.edu.sg

## Slide 3: WHAT’S GOING ON FOR THE NEXT 2-3 HOURS
Introduction of Ultra-wideband(UWB)
  History of UWB
  What is Ultra-wideband(UWB)?
  How does UWB work?
  Use Cases for UWB
Hands-on workshop
  Introduction to Murata UWB development board
  Set up software work environment on computer
  Communication between iPhone and UWB device

## Slide 4: History of Ultra-wideband(UWB)
1960s – was researched primarily for military radar in the U.S.
<1994 – was classified as a military secret
2002 – was approved for civilian use
2019 – was well recognized by society
  Apple-designed U1 TMKA75 UWB chip in iPhone 11
    Enhanced AirDrop
    Improved Directionality
    UWB now in the hands of the consumer
Picture Source: iPhone-11-UWB.png (1458×1486)

## Slide 5: What is Ultra-wideband (UWB)?
UWB is a wireless communication technology that operates over a wide frequency spectrum
  Uses impulse radio with extremely short pulses (~2ns)
  Has a very low power spectral density
  Operates in typical 3.1 - 10.6 GHz range
  Uses very wide channels(at least 500 MHz)
  Data rates of up to 27 Mbps (Bluetooth: 3Mbps Max)
Enables measurement of Time of Flight(ToF) of radio signals with sub-meter accuracy for ranging/location services and close-proximity communications
Picture Source: Spark Ultra-Wideband Technology | Spark UWB SPARK microsystems

## Slide 6: Features of UWB
High-precision ranging and positioning
High Security
Low Interference with other communications
Low power consumption

## Slide 7: How does UWB Ranging & Localization work?
UWB Ranging & Localization Components
  Anchor (Fixed Unit) – Measures location of Mobile Units
  Tag (mobile unit) – in motion
  Location engine/server
Virous Algorithms for Measurement
Anchor
Anchor
Anchor
Tag
Location Engine/Server

## Slide 8: UWB Ranging & Localization Algorithm
Time of Flight (ToF)
  SS-TWR (Single-sided Two-Way Ranging)
    Clock synchronization is required
  DS-TWR (Double-Sided Two-Way Ranging)
    No clock synchronization is required
    Simpler and higher precision measurement
Time Difference of Arrival (TDoA)
Anchor
Anchor
Anchor
Tag

## Slide 9: UWB Ranging & Localization Algorithm
Angle of Arrival (AoA)
  2D AoA with 2 Antennas
  3D AoA with 3 Antennas
Anchor
Tag

## Slide 10: Applications of UWB
Secure Access Control
  Smart car access with smartphone for keyless entry and remote start
  Can be combined with BLE for wake-up/initialization prior to secure ranging.
Secure Wireless payments
  More secure than NFC, and can leave smartphone in the pocket
Location-based Services
  Asset tracking in high density environments
  Proximity of small objects
  Sports & Fitness Tracking
    Tracking of players and athletes on a field/arena
Healthcare
  Medical radar
  Wireless Health sensors(WBAN)
Automotive
  Wireless in-vehicle Networks
  Smart Keys
Source: Spark Ultra-Wideband Technology | Spark UWB SPARK microsystems

## Slide 11: Application for B&O products
Locating speakers in the room
Directional or Spatial Sound
What is Your Idea?

## Slide 12: Hands-on Workshop

## Slide 13: Murata Type 2BP Evaluation Board

## Slide 14: Workshop
Go to the following Github link for instructions:
https://github.com/GrahamZhu-NUS/UWB-Workshop
python3 -m ensurepip

## Slide 15: What can be done Next?
Try more sample code and development instructions on "My Murata" Website
Develop Apps for UWB application
For IOS
For Android

## Slide 16: THANK YOU